## Slide 1: PWM-DRAWER
AMIT_Poject
ENG: Mohamed Mosaad

## Slide 2: INTRODUCTION
Pulse Width Modulation, a technique for controlling the average power delivered by an electrical signal.
PWM is used to generate analog signals from
digital devices, such as microcontrollers.
PWM works by switching the supply between on and off at a fast rate.

## Slide 3: PWM signal elements
Is represented through the total number of cycle per second.
Frequency
Is defined with respect to percentage or as a number between 0 & 1.
Duty cycle

## Slide 4: Layered Architecture
Application Layer
PWM_Drawer
Hardware Abstraction Layer
GLCD
Micro-Controller Abstraction Layer
DIO
GPT
PWM
ICU

## Slide 5: Flowchart
Measure_Signal
ICU_GetDutyCycle();
Initialization PWM_Init(); ICU_Init(); GLCD_Init();
Draw_Signal GLCD_DisplayString(); GLCD_DisplayFloatingPoint(); GLCD_DisplayInteger(); GLCD_DisplaySpecialPattern();

## Slide 6: Flowchart
Measure_Signal
ICU_GetDutyCycle();
Clear Input Capture Flag
Set Trigger Edge: RISING_EDGE
Wait for Input Capture → i.e. Start of Cycle
Clear Input Capture Flag and Timer Counter
Set Trigger Edge: FALLING_EDGE
Wait for Input Capture → i.e. High Count
Clear Input Capture Flag and Timer Counter Set Trigger Edge: RSING_EDGE
Wait for Input Capture → i.e. Low Count
𝑃𝑒𝑟𝑖𝑜𝑑 𝑇𝑖𝑚𝑒
𝐻𝑖𝑔h 𝑇𝑖𝑚𝑒
𝐷𝑢𝑡𝑦 𝐶𝑦𝑐𝑙𝑒 % = x100
3
𝐻𝑖𝑔ℎ 𝑇𝑖𝑚𝑒 𝑚s =𝐻𝑖𝑔ℎ 𝐶𝑜𝑢𝑛𝑡 ∗𝑃𝑟𝑒𝑠𝑐𝑎𝑙𝑒𝑟∗10
𝐹𝑐𝑝𝑢
period 𝑇𝑖𝑚𝑒 𝑚s
3
=(𝐻𝑖𝑔ℎ 𝐶𝑜𝑢𝑛𝑡+𝐿𝑜𝑤 𝐶𝑜𝑢𝑛𝑡) ∗𝑃𝑟𝑒𝑠𝑐𝑎𝑙𝑒𝑟∗10
𝐹𝑐𝑝𝑢

## Slide 7: Flowchart
Draw_Signal GLCD_DisplayString(); GLCD_DisplayFloatingPoint(); GLCD_DisplayInteger(); GLCD_DisplaySpecialPattern()
;
Choose a scale (milliseconds
to pixel) as 𝑝𝑒𝑟𝑖𝑜𝑑 𝑡𝑖𝑚𝑒
5
GLCD Line 0: Display Frequency Value in kHz.
GLCD Line 1: Display Duty Cycle Value in %
GLCD Line 4: Display Period Time Value in milliseconds.
GLCD Line 5: Display Arrow on First Cycle Period Time.
GLCD Line 6: Display the PWM signal shape.

## Slide 8: Flowchart
Draw_Signal GLCD_DisplayString(); GLCD_DisplayFloatingPoint(); GLCD_DisplayInteger(); GLCD_DisplaySpecialPattern()
;
GLCD Line 6: Display the PWM signal shape.
Repeat till max. pixel width (128)
Display Rising Edge Pattern
Repeat for
𝑝𝑒𝑟𝑖𝑜𝑑 𝑡𝑖𝑚𝑒
5
Display High Line Pattern
Display Falling Edge Pattern
Display High Line Pattern
Repeat for
𝐿𝑜𝑤 𝑡𝑖𝑚𝑒
𝑆𝑐𝑎𝑙𝑒

## Slide 9: THANKS!